## Slide 1
AI VISION
VIAD
VIAD: Vision Impaired Assistive Device
AI-Vision
Rayan Altawijari
431107823
Faris Alsuhibani
431107834
Mohammed Alsharekh
431108100
Mohaya Almutairi
431107802
Abdullah Alfayez
431108148
Supervised by: Dr. Ali Mustafa Qamar Khan
Qassim University · Department of Computer Science · 1447/1448 (2025/2026)
Presented by:

## Slide 2
Plan
AI Vision VIAD · Qassim University
2

## Slide 3
INTRODUCTION
AI Vision VIAD · Qassim University
3
01

## Slide 4
INTRODUCTION
The problem & the gap
295 million people live with moderate to severe vision impairment yet today's assistive tools each leave a critical gap.
White Cane
Detects only ground level obstacles within reach misses head level hazards like signs and branches occupies a hand.
GPS Navigation Apps
Give turn by turn routes outdoors, but offer no real time awareness of nearby objects or obstacles.
Commercial Smart Glasses
Camera recognition with voice output but cost upward of $2,000 and depend on a constant internet connection.
AI Vision VIAD · Qassim University
4

## Slide 5
INTRODUCTION
What VIAD is
A hands free wearable on a 3D-printed glasses frame, powered by a Raspberry Pi combining two complementary loops
Safety Loop (offline), always on
Continuously detects obstacles and speaks their name and distance.
Cognitive Loop (online), on demand
On a button press, answers a spoken question about the scene via cloud AI.
One affordable device immediate safety and on-demand understanding.
AI Vision VIAD · Qassim University
5

## Slide 6
PROJECT AIM Design and build an AI powered smart glasses system that detects surrounding objects in real time and guides visually impaired users through audio feedback.
01
Wearable Device Design
Comfortable frame integrating AI and computer vision
DONE
02
Real-time Object Detection
Detection of common obstacles and objects
DONE
03
Integrated Distance Sensing
Precise ultrasonic ranging for safe navigation
DONE
04
Audio Feedback System
Bilingual, offline + online voice guidance
DONE
05
Usability & Reliability
Intuitive, dependable, fail-safe operation
DONE
AI Vision VIAD · Qassim University
6
Aim & Objectives
02

## Slide 7
IMPLEMENTATION & EVALUATION
AI Vision VIAD · Qassim University
7
03

## Slide 8
IMPLEMENTATION & EVALUATION
Dual-loop, multithreaded architecture
AI Vision VIAD · Qassim University
8

## Slide 9
IMPLEMENTATION & EVALUATION
Hardware build
Fritzing wiring Pi 4B, HC-SR04, camera, mic & speaker
Raspberry Pi 4B
Main controller
HC-SR04 Ultrasonic
Bridge mount · GPIO 23/24
Tactile Button
GPIO 26 · triggers assistant
Pi Camera
CSI · live frames
Bluetooth Audio
Hands-free, private output
3D-Printed Wayfarer
Frame · 5V/3A power bank
GPIO via gpiozero · HC-SR04 Trig 23 / Echo 24 · Button 26 (pull-up)
AI Vision VIAD · Qassim University
9
bluetooth earbuds

## Slide 10
IMPLEMENTATION & EVALUATION
Software modules & threading
main.py
Orchestrator · voice language picker · data flow
hardware.py
gpiozero button + HC-SR04 distance sensor
vision.py
Picamera2 capture + LiteRT detection pipeline
assistant.py
Gemini 2.5 Flash multimodal queries (bilingual)
audio.py
Bilingual TTS neural cache + espeak-ng / STT
Multithreading
Background distance sensor thread (~20 Hz)
Non-blocking voice alert threads
Neural voice cache built in the background
Gemini call with a 15 s timeout
is_busy flag serializes the two loops
AI Vision VIAD · Qassim University
10

## Slide 11
IMPLEMENTATION & EVALUATION
Object detection & model decision
BASELINE
YOLOv11-Nano
24-class custom training · mAP@0.5 ≈ 0.71
Precision 0.82 . Highest accuracy in our tests but ran below real time on the Pi 4B CPU.
DEPLOYED
SSD-MobileNet
Quantized COCO · TFLite · real-time on Pi 4B
Fast enough for continuous safety the right trade-off for a wearable device.
~150 ms
Safety-loop latency
>80%
Detection confidence
Real-time
Continuous on-device inference
Edge benchmark accuracy vs. real time speed on Raspberry Pi 4B
AI Vision VIAD · Qassim University
11

## Slide 12
IMPLEMENTATION & EVALUATION
Edge benchmark & training results
On-device inference speed (Raspberry Pi 4)
Published benchmark, Alqahtani et al. (2024) [7] — lower is faster
YOLOv11-Nano training baseline
Custom dataset · 32,511 images · 24 navigation classes · 80 epochs
0.713
mAP@0.5
0.494
mAP@0.5:0.95
0.82
Precision
0.67
Recall
Strongest classes: stop signs, doors, fire hydrants 0.98 · crosswalks 0.95 · trees 0.94
AI Vision VIAD · Qassim University
12

## Slide 13
IMPLEMENTATION & EVALUATION
Cognitive loop (scene understanding)
Press the button to ask about the scene. VIAD captures what the camera sees and sends it with your spoken question to Gemini 2.5 Flash.
Button
GPIO 26 press
Listen
STT Google Web Speech
Capture
Live camera frame
Gemini 2.5 Flash
Frame + question
Speak
1–2 sentence answer
Resilient by design: a 15 s query timeout keeps the button alive if the network stalls · average response ≈ 2.5 s
AI Vision VIAD · Qassim University
13

## Slide 14
IMPLEMENTATION & EVALUATION
Bilingual audio feedback
Language by voice at startup
English or Arabic, chosen by speaking. Defaults to English on silence so launch never blocks.
DISTANCE-BUCKETED ALERT
“Careful, chair at 50 centimeters”
Object label fused with the ultrasonic distance, floor-bucketed to 10 cm. Triggered under 100 cm; alerts ≥ 4 s apart.
Two-tier text-to-speech
Tier 1 — cached neural voice
edge-tts Microsoft neural MP3s, pre-rendered once and replayed from disk at ~80 ms.
Tier 2 — instant fallback
espeak-ng speaks immediately if a phrase isn't cached fully offline, never silent.
Speech-in: Google Web Speech API (en-US / ar-SA)
AI Vision VIAD · Qassim University
14

## Slide 15
Python
Primary language
TensorFlow Lite
On-device inference
OpenCV
Image processing
gpiozero
GPIO control
Picamera2
Camera capture
SpeechRecognition
Google Web Speech API
edge-tts + espeak-ng
Neural TTS + fallback
google-genai
Gemini 2.5 Flash
threading
Concurrent dual loop
AI Vision VIAD · Qassim University
15
Technical tools & languages
04

## Slide 16
SYSTEM TESTING & RESULTS
AI Vision VIAD · Qassim University
16
05

## Slide 17
SYSTEM TESTING & RESULTS
Testing strategy
Unit testing
Each module in isolation
Ultrasonic + button via hardware test script
Live detector drawing test (boxes + confidence)
Audio & assistant modules verified separately
Integration testing
The dual loop under load
Concurrency Cognitive Loop never starves Safety
Pin-26 button debounce no accidental double-triggers
Thermal endurance 1 hour continuous detection
User acceptance
Real navigation scenarios
Static obstacle: chair at 1 m → fused proximity alert
Dynamic hazard: person crossing detected early
Cognitive query: Gemini describes a cluttered table
AI Vision VIAD · Qassim University
17

## Slide 18
SYSTEM TESTING & RESULTS
Measured results
~150 ms
Safety-loop latency
~2.5 s
Gemini response (avg)
>80%
Detection confidence
~68°C
CPU under load · no throttling
Sensor fusion = fail-safe redundancy
When the camera can't classify an object glass doors, low light the HC-SR04 still delivers a proximity warning. The user is never left unprotected.
AI Vision VIAD · Qassim University
18
Assembled prototype
Live detection output

## Slide 19
The speed accuracy trade-off
For a safety wearable, dependable real-time inference outweighs a few points of mAP so SSD-MobileNet was the right choice over the more accurate YOLO baseline.
Sensor fusion is the fail-safe
Pairing vision with ultrasonic ranging covers the perception gaps that defeat vision-only devices the system degrades gracefully, never silently.
Honest limitations
Battery life limits continuous all-day wear, and the Cognitive Loop needs connectivity though the Safety Loop remains fully offline.
AI Vision VIAD · Qassim University
19
DISCUSSION
06

## Slide 20
All five objectives achieved VIAD is built, tested, and working.
Edge + cloud, together
Offline Safety Loop for immediate protection; online Cognitive Loop for understanding.
Affordable & wearable
A Raspberry Pi and open tools deliver capability that commercial glasses charge thousands for.
Dependable by design
Sensor fusion and tiered audio keep the system safe even when one channel fails.
AI Vision VIAD · Qassim University
20
Conclusion
07

## Slide 21
①
Offline scene Q&A
Deploy a small language model on-device for visual question answering without internet better privacy and reliability.
②
GPS / GIS navigation
Add turn-by-turn outdoor guidance layered on top of real-time obstacle detection.
③
Haptic & bone-conduction
Vibration cues for obstacle direction; bone-conduction audio that keeps the ears open to the environment.
AI Vision VIAD · Qassim University
21
FUTURE WORK
08

## Slide 22
Questions & Answers
Thank you
AI Vision VIAD · Qassim University · Department of Computer Science · 1447/1448